Goal: Separate the UI from the synth modules in a modern way.

Base System

- All audio signals are fully analog (synth and effect modules may be using digital signal processing)

Synth (Generator) modules

- Up to 16 fully analog channels with automatic mixing
- Pluggable and interchangeable modules
- I²C Bus for digital control
- +15V, -15V, +5V

Effect modules
- Maximum of 16 effect modules
- 16 analog sends

# Generator Module
## Connector Specification
Standard 0.1” pitch 2x13 socket strip, 8mm height
## Pin Specification
- Pin 1: GND
- Pin 2: +5V
- Pin 3: -15V
- Pin 4: +15V
- Pin 5: I²C SDA
- Pin 6: I²C SDL
- Pin 7-10: Reserved
- Pin 11-26: Outputs 1-16

## Module Dimensions
- Maximum module height: 3cm
- Module width: 5cm
- Module length: 10cm
- 4 M3 screws are used for mounting the module. The corner distance of the M3 holes is specified with 5mm.
- Stacked modules (multiple PCBs) are allowed, as long as they don't exceed the maximum height of 3cm. In case of stacked modules, a edge distance of at least 5mm is required to allow the user to mount the module
## Interfacing
Initializing procedure: Send module serial number, capabilities (to be defined).